## Slide 1
🅿️
Smart Parking Finder
IoT Real-Time Parking Slot Monitor
ESP32
HC-SR04
Firebase
Web Dashboard
SDLC Project · B.Tech CSE (Cybersecurity) · SR University, Hyderabad
Notes: Introduce the project: a real-world IoT system that tells drivers which parking slots are free in real time, ending the "10 rounds around the market" problem.

## Slide 2
🚫 The Problem
10+
Rounds around the
market just to find
an empty slot
⏱️ Wasted Time
15–20 min spent searching for parking before entering the market
⛽ Fuel Waste
Unnecessary rounds burn fuel and increase CO₂ emissions
😤 Frustration
Zero visibility into which slots are occupied vs free
🚦 Congestion
Circling vehicles block lanes and slow down all traffic
"A smart city needs smart parking — real-time visibility eliminates the guesswork."
Notes: This is the "fix my itch" problem selected for the SDLC subject.

## Slide 3
✅ Our Solution
An IoT system that detects slot occupancy in real-time and displays it on a live web dashboard — so drivers know exactly where to park before they arrive.
📡
Live Detection
HC-SR04 sensors detect a car in <2 sec
🔥
Cloud Sync
ESP32 pushes data to Firebase over WiFi
🖥️
Dashboard
Color-coded live web dashboard for all 6 slots
🗺️
Navigation
Click a free slot → Google Maps turn-by-turn directions
Notes: Four pillars: detect, sync, display, navigate. End-to-end from physical sensor to phone map.

## Slide 4
🏗️ System Architecture
Sensor Layer
6× HC-SR04
Ultrasonic
Sensors
Voltage Divider
1kΩ + 2kΩ
per Echo pin
→
Processing
ESP32 DevKit
Dual Core 240MHz
Built-in WiFi
Arduino Firmware
Median Filter
+ Hysteresis
WiFi
Cloud
Firebase
Realtime DB
Singapore region
Anonymous Auth
JSON structure
/parking/slotN
→
Dashboard
Web Dashboard
HTML + JS
Live listener
Google Maps
Directions API
GPS navigation
Sensor → ESP32 (Arduino/C++) → WiFi → Firebase Realtime DB → Web Dashboard → Google Maps
Notes: Walk left to right. Each layer has two components. The WiFi hop is the only wireless step — everything else is wired or HTTP.

## Slide 5
🔧 Hardware Components (Bill of Materials)
🔲
ESP32 DevKit V1
Qty: ×1
240MHz dual-core · Built-in WiFi & BT · 3.3V GPIO · ADC-capable pins for Echo lines
📡
HC-SR04 Ultrasonic
Qty: ×6
2cm–400cm range · Outputs 5V Echo · Trig: direct to GPIO · Echo: via voltage divider
⚡
Voltage Divider
Qty: ×6
1kΩ in series + 2kΩ to GND per Echo pin · Steps 5V → 3.33V safe for ESP32 GPIO
🔌
5V Power Supply
Qty: ×1
Powers ESP32 via VIN (USB or adapter) · ESP32 VIN rail powers all 6 sensors
🧱
Breadboard + Wires
Qty: ×1
Prototyping breadboard · Shared power rails for VCC and GND across all sensors
💡
Red/Green LEDs
Qty: ×6
Optional physical indicator on physical demo model · Red=Filled, Green=Available
Notes: KEY POINT: The voltage divider on every Echo pin is mandatory. HC-SR04 outputs 5V but ESP32 GPIO is only 3.3V-tolerant. Skipping it causes gradual pin damage. 1kΩ + 2kΩ gives exactly 3.33V at the junction.

## Slide 6
💻 Software Stack
① Firmware Layer
Arduino IDE + C++ (ESP32)
→ HC-SR04 median filter — 5 samples, picks the middle value
→ Hysteresis: ENTER_CM 12 → filled, EXIT_CM 18 → empty (prevents flicker)
→ Write-on-change — Firebase push only when status actually changes
→ Mobizt Firebase library for ESP32 anonymous sign-in + RTDB writes
② Cloud Layer
Firebase Realtime Database
→ Project: smart-parking-60cdf · Region: asia-southeast1 (Singapore)
→ Anonymous Authentication enabled for ESP32 sign-in
→ JSON path: /parking/slot1 → { status, distance, slot, updated }
→ Security rules: read/write true for dev → lock to auth!=null for production
③ Frontend Layer
HTML5 + Vanilla JS + Firebase SDK v9
→ db.ref("/parking").on("value") — live listener, zero polling
→ Zone selector: All · North Wing · South Wing · Main Gate
→ 📍 Get Directions button: gets GPS → opens Google Maps to slot coords
→ Responsive design — works on desktop, tablet, and mobile browsers
Notes: Three clean layers. No React framework needed — plain HTML keeps it portable. Anyone can open the file in Chrome and see live data immediately without any install.

## Slide 7
⭐ Key Features
🔴🟢
Live Slot Status
Each slot card updates within 1–2 seconds. Green ✅ = Available, Red 🚗 = Filled. No page refresh needed — Firebase listener fires on every change.
🗺️
Zone Location Filter
3 zones (North Wing, South Wing, Main Gate). Selecting a zone filters cards AND recalculates the summary bar for that zone only.
📍
Google Maps Directions
Click "Get Directions" on any free slot. Browser requests your GPS location then opens turn-by-turn Maps navigation from you to that exact slot.
📊
Live Summary Bar
Always shows Total / Available / Filled count for the selected zone. Overview mini-cards show each zone's free count at a glance.
🛡️
Reliable Detection
Median filter (5 samples) eliminates noise. Hysteresis (12cm / 18cm thresholds) prevents rapid filled↔empty flicker at the boundary.
📱
Responsive Design
Dashboard adapts to desktop, tablet, and phone. No app install — just open the HTML file in any browser. Works offline once loaded.
Notes: Demo moment: click a green slot card → browser asks for location permission → Google Maps opens with turn-by-turn directions to that exact parking spot. That is the WOW feature for the audience.

## Slide 8
📋 SDLC Phases Applied
01
Planning
• Identified real problem: drivers waste 15–20 min searching for parking
• Scope defined: 6-slot IoT demo with web dashboard + navigation
• Feasibility: ESP32 + Firebase free tier keeps BOM cost low
02
Requirements
• FR: detect slot, display filled/empty, navigate to free slot in real-time
• NFR: ≤2s latency, reliable detection, responsive UI, scalable architecture
• SRS document with use-cases, DFDs, and data flow diagrams
03
Design
• 4-layer system architecture: Sensor → ESP32 → Firebase → Dashboard
• Database schema: /parking/slotN → {status, distance, slot, updated}
• UI wireframes: zone tabs, card grid, summary bar, directions button
04
Implementation
• ESP32 C++ firmware: sensor read → median filter → hysteresis → Firebase push
• Firebase: Realtime DB + Anonymous Auth + regional URL (asia-southeast1)
• Web dashboard: Firebase JS SDK listener + zone filter + Maps API
05
Testing
• Unit: individual sensor accuracy tested at 5cm, 12cm, 18cm, 30cm distances
• Integration: ESP32 → Firebase → dashboard data flow verified end-to-end
• Functional: slot6 FILLED/empty flip confirmed live on Serial Monitor
06
Deployment
• Firmware flashed via Arduino IDE (BOOT-button method, 115200 baud)
• Dashboard: portable single HTML file — no server or framework required
• Known gap: DB rules open for dev → restrict to auth!=null for production
Notes: This is the heart of the SDLC subject mark. Walk through each phase confidently. Emphasize FR vs NFR in requirements — this shows software engineering understanding. The "known gap" in deployment is good — it shows you understand production requirements.

## Slide 9
📊 Results & Live Demo
⬛ Serial Monitor — 115200 baud
19:06:18 → Connecting to WiFi: sanathraag
19:06:20 → WiFi connected. IP: 10.126.118.145
19:06:21 → Firebase sign-in OK
19:06:21 → Scanning slots...
19:06:22 → slot1 → empty (999 cm)
19:06:24 → slot2 → empty (999 cm)
19:10:41 → slot6 → FILLED (0 cm) ←
19:10:44 → slot6 → empty (999 cm)
19:11:00 → Scanning slots...
19:11:01 → slot1 → empty (999 cm)
✅ Project Milestones
CP2102 driver installed → COM11 detected
Firebase library compiled — 91% flash used
WiFi connected, real IP assigned
Firebase sign-in OK (Anonymous Auth)
Slot data live in Firebase Realtime DB
slot6 FILLED/empty detection proven
Zone filter + Maps directions working
Dashboard demo-ready for madam
Notes: Show this slide while doing the live demo on the laptop. Point to the serial monitor output from your actual testing session — the slot6 FILLED line is the money shot proving end-to-end works.

## Slide 10
🎯 Conclusion & Future Work
What We Delivered
✅ End-to-end IoT system: physical sensor → cloud → live dashboard
✅ Reliable detection: median filter + hysteresis eliminates false reads
✅ Zone-based slot finder with Google Maps turn-by-turn navigation
✅ Full SDLC coverage: planning → requirements → design → test → deploy
Future Enhancements
→ React Native Android APK
→ Computer vision (camera-based)
→ Slot pre-booking + payment
→ Multi-floor parking support
⚠ Known Limitations
DB rules open (read/write: true) → restrict to auth!=null before production deployment.
HC-SR04 affected by temperature/humidity outdoors → use weatherproof sensors for real parking lots.
Tech Stack Used
ESP32 · HC-SR04 · Arduino IDE
Firebase RTDB · HTML / JavaScript
Google Maps Directions API
Thank You 🙏
Notes: Wrap up in 2 minutes. Mention the known limitation — open DB rules — as a planned production hardening step. Offer to do a live demo showing the slot flipping on the serial monitor and dashboard simultaneously.